## Slide 1: Redundancy and Emergency Interconnectivity Study Water Transmission Grid Study
For the Coosa North Georgia Region
April 22, 2015
Presented by: Michelle Vincent, Jacobs and Tanya Kinnard, Amec Foster Wheeler

## Slide 2: Introduction
Background
Redundancy and Emergency Interconnectivity Study
  Service Areas
  Existing interconnections
  Emergency scenarios and reliability targets for focus area
  Additional interconnection projects and costs
  Next steps and recommendations
Water Transmission Grid Study
  Methods and priorities
  Conceptual grid development
  Potential sources
  Recommendations and costs
  Future Activities

## Slide 3: Background
Studies were commissioned by the Coosa North Georgia Regional Water Planning Council (“Council”) to support Regional Water Plan implementation efforts
The Council:
  Established by Georgia's State Water Plan in 2008
  Sets direction, goals, and policy for water planning in the region
  Works closely with Georgia Environmental Protection Division to produce Regional Water Plans and support implementation
  Meets semi-annually to quarterly
The North Georgia Water Partnership (“Partnership”) serves as the technical advisory body for the Council, in addition to implementing goals for water planning and service for the region.
The Partnership:
  Formed in 2003
  Provides proactive regional water-based planning, technical assistance and education
  Meets monthly and assists with implementation process

## Slide 4: Background
Coosa North Georgia Water Planning Region
River basins: Tennessee, Coosa, Chattahoochee, Savannah

## Slide 5: Redundancy and Emergency Interconnectivity
Major tasks of Study:
Data collection
Determine Service Areas - entire region
Analyze and map existing interconnections – focus area
Evaluate emergency scenarios and reliability targets for focus area
Propose additional interconnection projects
Next steps and recommendations

## Slide 6: Redundancy and Emergency Interconnectivity
Public Water Service Areas
Notes: Determined and mapped service areas for region

## Slide 7: Redundancy and Emergency Interconnectivity
Modeled after study commissioned by GEFA for the Metro Atlanta area
Goal is to eventually cover entire Coosa Region and incorporate appropriate findings and targets into Regional Plan
Initial Focus Areas
  Chatsworth
  Dalton
  Rome (Floyd County)
  Calhoun
Focus area prioritized due to:
  High levels of existing interconnections,
  Known availability of GIS data
  Centralized location.

## Slide 8: Redundancy and Emergency Interconnectivity
Data collection
Analysed and mapped existing interconnections
Focus Areas already interconnected
Notes: Collected data, pipes, water mains, water treatment plan capacities, permit limits, water availability. Demand – current (2010) and 2050 – from Regional Water Plan
Red dots are existing; orange are proposed.

## Slide 9: Redundancy and Emergency Interconnectivity
Compared existing and future (2050) demand of Annual Average Day demand with water availability
Calhoun’s current supplies would not meet 2050 demand
Meeting existing and future demand
Focus Area results:
System | Annual Average Day – 2010 Demand | Annual Average Day – 2050 Demand
Chatsworth |  | 
Dalton |  | 
Rome |  | 
Calhoun |  | X
Notes: For purposes of interconnection plan, we assume that Calhoun will expand or build new water treatment facility to meet demand.

## Slide 10: Redundancy and Emergency Interconnectivity
Emergency Scenarios:
  Failure of largest treatment facility within a Partnership member’s system
  Short-term catastrophic failure of distribution system
  Short-term contamination of a water supply system
  Short-term contamination of a raw water source
Reliability Targets and Emergency Scenarios
Reliability Targets
  100% Annual Average Day Demand
  65% Annual Average Day Demand
  35% Annual Average Day Demand

## Slide 11: Redundancy and Emergency Interconnectivity
Reliability Targets and Emergency Scenarios
System | 65% of Immediate Demand | 35 % of Immediate Demand | 65% of 2050 Demand | 35% of 2050 Demand
Chatsworth |  |  |  | 
Dalton |  |  | 2.0 MGD | 
Rome |  |  | 2.5 MGD | 
Calhoun |  |  |  | 
Maximum Deficit, for evaluated emergency planning scenarios:
Dalton and Rome: Failure of largest water treatment facility or short-term failure of water distribution system.

## Slide 12: Redundancy and Emergency Interconnectivity
Proposed additional interconnection projects
Notes: Red dots are existing; orange are proposed.

## Slide 13: Redundancy and Emergency Interconnectivity
Range of cost ~$10,000 to $230,000 based on length
Notes: Proposed projects and estimated costs

## Slide 14: Redundancy and Emergency Interconnectivity
Next steps and Future Activities:
  Phase 1 (current Project): Rome/Floyd, Chatsworth, Dalton, Calhoun [Completed]
  Phase 2: Dade, Walker, Catoosa, Chattooga, Polk, (Tennessee) (2016)
  Phase 3: Gilmer, Murray, Pickens, Dawson, (Big Canoe), (Tennessee),(connections with Cherokee Co and Metro Influence) (2017)
  Phase 4: Fannin, Union, Lumpkin, (Tennessee) (2018)
  Phase 5: Towns, White, Habersham (2019)
  Phase 6: Compile entire region (2020)
Notes: Each phase take about 6-9 months, but could be delayed due to budget concerns. Coucld also accelerate timeframe by combining phases.

## Slide 15: Water Transmission Grid Study

## Slide 16: Water Transmission Grid
Methods and priorities
  Worked with Partnership to determine potential water supply sources
  Collected regional data
  Evaluated
    raw vs. finished water
    open and/or natural channels vs closed (pipes) channels
  Proposed Beyond 2050 Conceptual Grid system
    Long term planning approach
    hybrid system – majority finished water.
    Features (5) “service” zones

## Slide 17: Grid Concept Development
Envisioned as one continuous raw or finished pipeline available for anyone to tap
Refined to (4) service zones in GA and (1) service zone in TN
Reality of these endeavors is beyond 2050 as water supply projected needs are minimal through 2050 for the region
Planning for 3rd generation

## Slide 18: Conceptual Water Transmission Grid
(Zone 1) - North Blue Ridge
(Zone 2) -Shoal Creek-Upper Chattahoochee
(Zone 3) - Carters Lake-Coosawattee
(Zone 4) - Tennessee Finished Water
(Zone 5) - West Georgia Interconnect

## Slide 19: Conceptual Water Transmission Grid

## Slide 20: Potential Water Supply Sources
Tennessee Water Systems
  Interconnections already exist (Tennessee American Water and Eastside Utility)
  Several GA municipalities and communities currently purchase water from TN
  Use of finished water avoids controversy

## Slide 21: Potential Water Supply Sources
Rome/Dalton/Calhoun
  Surplus water available now and near future
  As part of Redundancy and Emergency Interconnectivity Study this focus area is identified as an example for the region and possible the state
    Highly interconnected already

## Slide 22: Potential Water Supply Sources
Regal Springs
  A well and surface water spring system
  Benefits include requiring minimal treatment
  and conveniently located to west side of region

## Slide 23: Potential Water Supply Sources
Lake Blue Ridge
  Blue Ridge was chosen over Nottley or Chattuge due to proximity to future water needs
  Conceptual grid envisions future connection to other lakes in the area

## Slide 24: Potential Water Supply Sources
Proposed Reservoir on Dry Creek
  Identified in “Preliminary Water Supply Study Technical Memorandum” by Partnership in 2008
  Projected yield ~ 12.2 MGD
  Located between Catoosa and Whitfield counties
  One of highest rated potential reservoirs

## Slide 25: Potential Water Supply Sources
Shoal Creek Reservoir
  Potential yield 100 MGD
  Proximity to southern and eastern Coosa region
  Eliminates moving water through difficult terrain

## Slide 26: Recommendations and Costs
Closed pipelines to transport water
Break region into interconnected zones
Move water through path of least resistance
Costs for these types of project pipeline scenarios range from $17M to $58M per zone or on average at $11M per pipeline length
Similar projects around the world range from $100s of millions to $1 billion

## Slide 27: Operation of Grid
Grid Operation
Proposed “Chain Memorandum of Understanding” (MOU)
Allows existing agreement to remain and additional agreements to be added later
Agreements clarify how water will be transported throughout a zone

## Slide 28: Water Transmission Grid
Future Activities:
Incorporate additional interconnection areas
Collect additional data: utilities corridors.
Identify future regional water supply projects
Establish regional goals
  Target emergency redundancy rates 35% and 65%?
  Local and regional systems work to achieve goals.

## Slide 29: Comments, Questions and Discussion
Michelle Vincent, Jacobs and Tanya Kinnard, Amec Foster Wheeler