## Slide 1: Nutrient Trading Framework in the Coosa Basin
April 22, 2015

## Slide 2: Today’s Outline
Background Timeline
Nutrient Trading
Example Trade
Feasibility Study
Monitoring Plan
Questions?

## Slide 3
Water Environment & Technology September 2014

## Slide 4: Timeline
2008 - Lake Weiss TMDL (USEPA)
2010 – 1 mg/L TP limits in NPDES permits (GAEPD)
2011- Partnership and GAEPD Correspondence
2011 - 319 Grant Awarded to Evaluate Nutrient Trading
2012-2013 – Nutrient Trading in the Coosa Basin: A Feasibility Study
Dec. 2013 – Review with GAEPD
2014 – Pilot Nutrient Trading Monitoring Plan
Oct. 2014 – Review with GAEPD
2015 – Implement Monitoring Plan

## Slide 5: Background
Lake Weiss TMDL (USEPA 2008)
In order to meet Alabama Chlorophyll a standards, total phosphorus (TP) reduction targets set
GA required to reduce TP load by 30% at GA/AL state line
Goal can be met “any number of ways”
Source: USEPA 2008
5,273 Square Mile Drainage Area

## Slide 6: Background
Chart: 
| NPS | PS
 | 2280 | 930
Non-Point Sources
> 70%
  GAEPD issued TP permit limits for NPDES discharges of 1.0 mg/L (major) and 8.34 lbs/day (minor)
  Cost of NPDES permit holder compliance estimated to be millions of dollars
  Limits on Point Sources not targeting majority of the problem
  Feasibility Study to look at Nutrient Trading in Coosa Basin USEPA 319(h) grant
Coosa River Basin:
Total Phosphorus Load
Notes: Regulatory hook

## Slide 7: What is Nutrient Trading?
Tool to cost effectively meet pollution reduction goals
Notes: Meet watershed goals, using most cost effective practices.

## Slide 8: Trading Framework Examples
Neuse River, North Carolina
  Point to point source trades, nitrogen
Boise, Idaho
  Point to non-point source trades, phosphorus
Virginia Chesapeake Bay
  Many types of trades, both nitrogen and phosphorus

## Slide 9: Neuse River Trading & Offset Program
Point-point trading framework
20+ Neuse River Compliance Association Members can comply by meeting:
  Individual nutrient allocation; OR
  Aggregate allocation
Member have reduced nutrient discharges approx 70%
If allocations exceeded, must trade or pay into Wetlands Restoration Fund
Notes: Private watershed association

## Slide 10: Lower Boise River

## Slide 11: Benefit and Cost of Incremental P-Removal
0
1000
2000
3000
200
70
Level of Treatment (ug TP/L)
Lbs TP/day removed
0
25
50
75
100
125
150
175
200
225
250
275
300
Cost of Removal ($M)
Lbs TP/day Removed
Incremental Cost of
Removal ($M)
Trading Can Offer Significant Cost Benefits
Cost for additional 3% TP reduction = $40 million

## Slide 12: Background: Proposed Coosa Basin Trading Framework
Trades between individual parties
Trade terms and conditions incorporated into individual NPDES permits
Develop basic trading guidance
GAEPD to review/approve the trading guidance and NPDES permits
Stakeholder Meetings/Public Input
Notes: Don’t’ ask the state to set up new program, don’t set up a new organization, use existing authority in NPDES permits

## Slide 13: Nutrient Trading Overview
Non-Point Load Reduction
Point Source
Load Reduction
Trade
Trading Guidance
Permit Condition
$
Public Input
$

## Slide 14: Feasibility Study
Point source costs
Nonpoint source BMPs
Point source estimating tool
BMP estimating tool
Example Trade
Final Report Issued October 2013
http://www.ngawater.org
Notes: Demand and supply exists for a trade

## Slide 15: Example Trade: City of Calhoun
Adjusted goal 0.75 mg/L
Alum treatment
Limited capital costs under existing flow and limits
1.6 tons/yr additional sludge disposal
Annual O&M costs confirmed
$1.2 million capital and O&M over five years

## Slide 16: Example Trade Potential BMPs
Single BMP
  Enhanced Wetland/Chemical Treatment
Multiple BMPs
  Georgia Soil and Water Conservation Commission Manual
  Georgia Stormwater Manual
Source Reduction
  Poultry litter export
  Sludge land application

## Slide 17: Source Reduction: Poultry Litter Export
Traditional BMPs could not meet the full load reduction
Poultry litter has volume and concentration needed (UGA literature)
Poultry production is significant in Gordon County/City of Calhoun
Current demand for litter as fertilizer
Litter applied for Nitrogen, may be over applied for Phosphorus

## Slide 18
The City of Calhoun is willing to serve as an example point source facility for a potential trade.
Current Flow – 6 MGD
Current Effluent TP Concentration – 5 mg/L
Current Annual Mass TP – 93,030 lbs/yr
Permit Limit Flow – 16 MGD
Permit Limit TP Concentration – 1 mg/L
Permit Limit Mass TP - 48,735 lbs/yr
Load reduction needed 44,295 lbs/yr
This number will increase as flow increases.
$1.2 million to meet this load reduction at the plant
using alum over a five year period.
Trade Example: Point Source Data

## Slide 19
A typical Broiler House produces 180 tons of litter per year, or 360,000 pounds per year.
The phosphorus content (as P2O5) is approximately 3% of the litter = about 4,750 pounds/yr/house.
TP Pounds Needed per year – 44,295
TP Pounds Needed per year using Litter – 3,355,682
TP Tons Needed per year – 1,678
Safety Factor (20%) – 2,013
Cost to Purchase at $25 per ton - $50,335
Cost to Purchase over Five Years - $251,676
Does not include delivery factor to stream
Conversion Factors
0.0132 3% P2O5 in litter, convert to P
Trade Example: Poultry Litter Export

## Slide 20
Existing Poultry Litter Trade exists – how to participate in market http://www.galitter.org/
Verification of transport out of the basin
Minimum Standard for seller: Nutrient Management Plan
Permit Conditions – 5 year cycle, documentation, verification
Litter TP content confirmed
Documentation of TP reduction
Trading Issues to Consider

## Slide 21: Pilot Nutrient Trading Monitoring Plan
Goals
  Defensible monitoring plan
  Effectiveness of litter export
  Reduce variables
Issues
    Variability – watersheds, rainfall, upstream contribution
    Saturated soils, may take years to see TP reduction
Sampling Scenarios Considered –
  In-stream: Upstream/downstream of test fields
  In-stream: Comparison watersheds
  Field: Watershed sampling
  Field: Plot sampling
Notes: Robust for permit approval, UGA input, SQAP – used EPDs water quality monitoring SQAP. Time and expense considerations in accouting for variables in soils, rainfall, land use, slope, upstream water quality, etc.

## Slide 24: Next Steps
Monitoring Plan - 2014
Initiate monitoring 2015-2016
EPD Feedback – plots okay, larger field scale

## Slide 25: Questions?
Laurie Hawks Jerry Crawford
Brown and Caldwell City of Calhoun
lhawks@brwncald.com JCrawford@calnet-ga.net
678-231-6433 706-602-6078
Contact Information